## Slide 1
xxx
xxx
xxx
xxx
CONTINUE
xxx

## Slide 2
xxx
xxx
xxx
Recall, total molar flux of A in z-direction in a binary mixture at some point “z” for 1D case is:
Another way to view NA:
Notes: This formula for diffusive flux is based on the molar avg velocity of the fluid ie N = C* Vmol avg.

## Slide 3
xxx
xxx
xxx
xxx
xxx
xxx
An inline mixer adds increasing but small amounts of gas A to a stream of pure gas B flowing into a pipe.
Suddenly, valves at either end of the pipe slam shut and flow stops.
This traps a conc profile of dilute A in the pipe the moment after the flow stops:
What is the total molar flux of A in the z direction at point z1 at that moment? (Note that N = NA + NB .)
A C
B D
After the valves shut, total molar flux N of mixture is zero, so convective flux of A becomes zero.
There is only diffusional flux and it is given by Fick’s Law.
Notes: Chromatographers call this device, appropriately, a gradient maker

## Slide 4
xxx
xxx
xxx
xxx
NEXT - Special cases for mass transfer
Cases that follow are:
1D diffusion with negligible convection for binary (two-component) system
1D diffusion with convection for binary system
Unsteady state 1D diffusion with negligible convection
Each can be solved exactly to give MT fluxes and conc profiles
Case 1 is analogous to heat transfer by conduction
Case 2 has no analogy in heat transfer
Equimolar counterdiffusion fits with Case 1, and is topic of a HW problem
xxx

## Slide 5
xxx
xxx
CASE 1: Diffusion with negligible convection
xxx
xxx
EXAMPLE: slow evaporation of a liquid through quiescent gas (no convection currents).
Find total flux of A in tube and find conc profile of A in the tube.
Pure liquid A
Membrane super- permeable to A and B
High-speed sweep of pure B
Which is true?
A: equimolar counterdiffusion, i.e. N=0
B: dilute A
NB is zero (i.e. B is stagnant in tube), but NA is nonzero , so N is nonzero.
Sometimes called unimolecular diffusion.
Fn of membrane?
Allows mass transfer through it but keeps gas sweep from disturbing gas in tube.
So, stops convection currents in tube.
How would currents affect MT rate?
Make MT faster (by adding convective MT)
xxx
xxx
xxx

## Slide 6
Rapid sweep of pure B gas takes away molecules of A as they cross membrane, which dilutes A to “zero”.
System at temp T, pressure Ptot
xxx
CASE 1 CONTD: slow evaporation of a liquid through quiescent (no convection currents) gas
Pure liquid A
Membrane super- permeable to A and B
High-speed sweep of pure B gas
What is mol frac of A on gas side at liquid-gas interface?
A: yA = 0
B: yA = H xA / Ptot C: yA = (VP)A / Ptot
D: yA = 1
LOCAL EQUILIBRIUM at interface between A in liquid and A in gas.
Partial pressure of A at interface is its vapor pressure, given liquid is pure A.
If liquid were a mixture of A and a little B then yA would be lower:
Henry’s law (answer B) only valid for xA → 0 and here xA = 1.
Evaporating liquid itself, not removing dissolved gas from a liquid.
What is mol frac of A at membrane outer surface?
A: yA = 0 B: yA = H xA / Ptot C: yA = 1
xxx
xxx
xxx
z = 0
z = L
Now have boundary conditions at z=0 and z=L for differential equation for yA as fn of z, so can solve it …..

## Slide 7
System at temp T, pressure Ptot
Solve eqn to get:
xxx
Find conc profile of A in the tube.
Pure liquid A
Membrane super- permeable to A and B
High-speed sweep of pure B gas
Assume pseudo-steady state because evap rate is “slow”:
Slow evap → slow change in liquid level → at any moment conc profile approximates true steady state profile (where liquid level is unchanging).
z = 0
z = L
xxx
Assumed DAB independent of mixture compo, only fn of T and P.
Pretty true for gas mixtures.
xxx
xxx
z
yA
CASE 1 CONTD: slow evaporation of a liquid through quiescent (no convection currents) gas

## Slide 8
xxx
xxx
xxx
xxx
xxx
The total flux of A is:
Plausible: NA goes up as DAB or (VP)A get bigger or L gets shorter.
Note NA does not depend on z in tube; if it did…
… would violate steady state.
How did we get this formula?
Put our profile for yA(z) into our original eqn for NA and evaluated it.
CASE 1 CONTD: slow evaporation of a liquid through quiescent (no convection currents) gas
Find total flux of A in tube:
Pure liquid A
z = 0
z = L
High-speed sweep of pure B gas

## Slide 9
xxx
xxx
It’s true that NA goes up with T, but our formula starts to under-predict actual NA as we crank up the temp.
Why?
We can no longer neglect convective flux term:
(for 1D binary diffusion of gas in a tube at slow rates of evaporation)
xxx
What happens to NA if we crank up the system temperature?
A: NA goes down B: unchanged C: goes up
Effects of increasing T:
Molar conc of mixture Cm goes DOWN in inverse proportion to absolute temp (ideal gas law)
DAB goes UP because gas molecule speed goes up with T
(VP)A zooms UP, strong exponential dependence on T (which makes the yA profile steeper)
Element 3 dominates: NA goes up as T goes up.
pure B gas
z = 0
z = L
Recall that yA = (VP)A / Ptot

## Slide 10
xxx
xxx
Terms cancel provided DAB = DBA for a given compo, WHICH IS ALWAYS TRUE, AN IDENTITY.
Isn’t there a gradient dyB/dz in the tube, so isn’t there diffusive flux of B? Then B is NOT STAGNANT.
Nope, B is stagnant.
That diffusive flux of B is matched by an equal and opposite convective flux of B that makes NB = 0.
Eqn for NB:
xxx
CASE 2: Re-do tube problem with convection added back
Again, gas B in tube is STAGNANT: NB = 0
In tube at pseudo-steady state, B molecules have nowhere to go – they are not dissolving in the liquid A and they are not leaving out the membrane.
They are STAGNANT, spectators to the A molecules moving by.
pure B gas
z = 0
z = L

## Slide 11
xxx
xxx
xxx
xxx
CONTINUE 002
xxx

## Slide 12
xxx
xxx
For Case 2, where is NA highest?
A: near z=0
B: near z = L
C: NA is same for all z
Same as for Case 1.
To have steady state, NA has to be uniform along z or else A would accumulate somewhere in tube.
Solve the new ODE w convection of A included to get flux,
xxx
CASE 2: Re-do tube problem with convection added back (contd)
and conc profile,
With convection of A no longer negligible, profile bends.
z
yA

## Slide 13
xxx
xxx
Remember the eqn for total flux of A for 1D binary system:
yA is lowest near z= L and dyA/dz is steepest, so diffusive flux dominates.
The reverse is true near z=0 so convective flux is important there.
The arc shape of “convec” profile indicates changing proportions of diffusive flux of A and convective flux of A.
How do proportions shift?
xxx
Re-do tube problem with convection added back
z
yA
 | Near z=0 | Near z = L
Click A | diffusive flux of A dominates | convective flux of A dominates
Click B | convective flux of A dominates | diffusive flux of A dominates

## Slide 14
xxx
xxx
xxx
xxx
CONTINUE 001
xxx