## Slide 1: Equation Development: Assumptions
Steady state
Air is an ideal gas
Constant heat capacity
Constant ambient temperature and pressure

## Slide 2: Equation Development: Calibrating Rotameter
Flow rates were recorded in CFM, and converted to SCFM. Equation (1) was obtained from Rotameter Specifications by Omega.
Flow rates were converted to SCFM to calculate mass flow rates using the density of air at STP (2).
It was assumed that the outlet flow rate rotameter readings were correct

## Slide 3: Equation Development: Comparing Effectiveness of Operating Conditions
The difference between the hot and cold mass flow rates and temperatures was calculated in order to graphically analyze the relationship between the change in mass flow rate and temperature (3) and (4).
Cooling capacity was calculated to determine the effectiveness of the device (5)

## Slide 4: Equation Development: Verifying Laws of Thermodynamics
Assuming ideal gas behavior, the change in entropy was calculated at the inlet and outlets (6) using the inlet properties as reference temperature and pressure .
The overall entropy change was calculated using values from (6). This was calculated in order to find the rate of entropy production.

## Slide 5: Equation Development: Verifying Laws of Thermodynamics
The rate of heat lost/gained was calculated using the inlet temperature as a reference (8), was derived from an enthalpy balance on the system.
Qdot and ΔSoverall were used to calculate the rate of entropy generation (9), which was obtained from an entropy balance on the vortex tube.
In order for the second law of thermodynamics to hold δS must be greater than zero.