## Slide 1
Liquid water is in vapor-liquid equilibrium at 1.2 bar with water vapor and air in a piston-cylinder. When half the air is removed through a selective membrane (no water leaves) ________ of the water _______.
Pressure and temperature are constant.
all, vaporizes
all, condenses
some, vaporizes
some, condenses
vapor
air
liquid
1 kg
Notes: ANSWER: D
The partial pressure of water does not change and the partial pressure of air must stay the same since the total pressure is fixed. The volume of the gas must decrease; therefore, some water condenses.

## Slide 2
Liquid water is in vapor-liquid equilibrium at 1.2 bar with water vapor and air in a piston-cylinder. When all the air is removed through a selective membrane and half the water vapor is also removed, _______ of the water ____________.
Pressure and temperature
are constant.
all, vaporizes
all, condenses
some, vaporizes
some, condenses
vapor
liquid
1 kg
vapor
Notes: ANSWER: B
Since all the air is removed, but the total pressure remains at 1.2 bar, the pressure is greater than the partial pressure of water, which is less than 1.2 because in the original state the pressure of air plus water add to 1.2 bar. Thus, all the water condenses.

## Slide 3
A piston-cylinder at 45oC and below atmospheric
pressure contains 0.9 mol of n-hexane liquid and
0.1 mol of n-hexane vapor in equilibrium. When weights are removed from the piston to decrease the pressure to 99% of its original value at constant temperature, ____________________.
some of the liquid evaporates
most of the liquid evaporates
all the liquid evaporates
all the vapor condenses
some of the vapor condenses
vapor
liquid
1 kg
Notes: ANSWER: C
Since the temperature is constant and the system was originally at the saturation pressure for 45oC, if the pressure is decreased, the system will try to reach equilibrium by getting back to its vapor pressure by evaporating liquid. It will never get back to the original pressure since the pressure of the piston is lower than saturation pressure.

## Slide 4
Liquid water is in equilibrium with air at 50°C in a
fixed-volume container at 1 bar. The temperature is
lowered to 40°C. The partial pressure of the air ___________.
increases
decreases
remains the same
not enough information
vapor
liquid
Notes: ANSWER: B
The partial pressure of the air decreases because the temperature decreases (ideal gas law).

## Slide 5
A piston-cylinder contains liquid water in equilibrium with air at 1 bar and 40°C. Water vapor is injected into the system and allowed to equilibrate to 40°C.
What happens to the injected water vapor?
All of it condenses
All of it stays in the vapor phase
Some of it condenses
liquid
1 kg
vapor
vapor
Notes: ANSWER: A
The temperature does not change. The saturation pressure stays the same and all the water vapor that was added condenses to return to the saturation pressure by the time the system equilibrates.

## Slide 6
Water is in vapor-liquid equilibrium at 1.2 bar in a piston-cylinder. When 5 cm3 of air is injected into the system at constant pressure and temperature, _____ of the water ___________ .
all, vaporizes
all, vapor condenses
some, vaporizes
some, vapor condenses
vapor
liquid
1 kg
air
Notes: ANSWER: A
The total pressure is 1.2 bar and the saturation pressure of water is 1.2 bar. Once air is injected into the system, the partial pressure of water is less than 1.2 bar so no liquid water will be present at equilibrium.

## Slide 7
A
B
C
D
A piston-cylinder contains air and water vapor (10% relative humidity). Which is the correct plot of partial pressure of water versus total pressure, as the total pressure applied to the gas increases at constant temperature?
Ptotal
PH2O
Ptotal
PH2O
Ptotal
PH2O
Ptotal
PH2O
air &
water
vapor
Notes: ANSWER: A
As the total pressure increases, the partial pressure of water increases until the saturation pressure is reached. The water partial pressure then remains constant.